## Slide 1: DEPARTMENT OF ELECTRONICS AND COMMUNICATION DESIGN OF REAL TIME SPEECH RECOGNITION SYSTEM VIII SEMESTER SESSION: JAN – JUN 2017
SUBMITTED BY: GUIDE:
DHANANJAY KUMAR K L (1PI13EC030) Dr.MANIKANDAN J
KARAN G BARHANPUR (1PI13EC039) Professor, ECE Dept
KIRAN UDAY PAI (1PI13EC041)

## Slide 2: METHODOLOGY

## Slide 3: FEATURE EXTRACTION
MFCC
Frame the signal into short frames.
For each frame calculate the periodogram estimate of the power spectrum.
Apply the Mel filter bank to the power spectra, sum the energy in each filter.
Take the logarithm of all filter bank energies.
Take the DCT of the log filter bank energies.
Keep DCT coefficients 2-13, discard the rest.

## Slide 4: MFCC FLOWCHART

## Slide 5: DISCRETE COSINE TRANSFORM
The Discrete Cosine Transform (DCT) of the 26 log filter bank energies is taken to give 26 cepstral coefficients.
For ASR, only the 12 of the 26 coefficients are kept.

## Slide 6: DCT COEFFICIENTS

## Slide 7: DELTA COEFFICIENTS CALCULATION
Delta coefficients are calculated using the formula
cti =ct+1i - ct-1i
where i varies from 1 to 26 and t represents frame number

## Slide 8: DIFFERENT WAYS OF CLASSIFICATION
Three different ways
Eucledean Classifier using Filterbanks
SVM classifier using Filterbanks
SVM classifier using MFCC and Delta coefficients

## Slide 9: EUCLIDEAN CLASSIFIER USING FILTERBANKS
Filterbank which has maximum power for each Frame is computed.
For every frame if the power is above some threshold we retain the filter bank number.
Else set the filter bank number to zero.
Now this data is stored as a array of frames.
We use this array as the reference matrix

## Slide 10: EUCLIDEAN CLASSIFIER USING FILTERBANKS
Eucledean distance is calculated using the formula
The obtained array is compared with the reference matrix.
The index of the array with minimum distance is displayed.
The efficiency was found to be 65-70%

## Slide 11: FILTERBANK ARRAY FOR DIGIT ZERO

## Slide 12: FILTERBANK ARRAY FOR DIGIT ONE

## Slide 13: FILTERBANK ARRAY FOR OTHER DIGITS

## Slide 14: PHONEMES
A phoneme is a unit of sound in speech.
A phoneme doesn't have any inherent meaning by itself.
But when you put phonemes together, they can make words.
The third technique is based on this approach

## Slide 15: PHONEMES FOR DIGITS

## Slide 16: DIGIT RECOGNITION USING PHONETIC APPROACH
Here we use two SVM classifiers.
One to extract the phonemes.
Second to detect the digits based on the extracted phonemes.
A total of 17 phonemes are detected for digits 0 to 9.
Our first classifier detects the phonemes from the speech.
Second classifier then detects the digits based on the phonemes obtained.

## Slide 17: PHONEMES EXTRACTION
ZERO=ZE_IY_RO

## Slide 18: ONE

## Slide 21: THANK YOU